## Slide 1: TCP/IP Basics
Chapter 6

## Slide 2: Objectives
Describe how the TCP/IP protocol suite works
Explain CIDR and subnetting
Describe the functions of static and dynamic IP addresses

## Slide 3: Historical/Conceptual
Standardizing Networking Technology

## Slide 4: Early Days of Networking Software (1 of 2)
Several competing standards
Protocols: individual rules used by software
Protocol suites: many protocols lumped together
  Novell Netware: IPX/SPX
  Microsoft: NetBIOS/NetBEUI
  Apple: AppleTalk
  UNIX: TCP/IP

## Slide 5: Early Days of Networking Software (2 of 2)
TCP/IP won out as the protocol of choice
  Only protocol on the CompTIA Network+ exam

## Slide 6: Test Specific
The TCP/IP Protocol Suite

## Slide 7: The TCP/IP Model (1 of 3)
Introduced in Chapter 1
Top three layers
  Internet, Transport, and Application

## Slide 8: The TCP/IP Model (2 of 3)
Figure 6.1 The Link layer is important, but it’s not part of the TCP/IP protocol suite

## Slide 9: The TCP/IP Model (3 of 3)
Figure 6.2 The TCP/IP protocol suite redux
Notes: Note (p. 132): The TCP/IP protocol suite consists of thousands of different protocols doing thousands of different things. For the most part, the rest of this book discusses TCP/IP protocols. Right now, my goal is to give you an idea of which protocols go where in the TCP/IP protocol suite.

## Slide 10: The IP Packet (1 of 2)
Parts of an IP packet fit perfectly into layers of the TCP/IP model
Header for a higher layer is part of the data for a lower layer
  Example: a packet’s payload can be a TCP segment that consists of data from the layers above and a sequence number

## Slide 11: The IP Packet (2 of 2)
Figure 6.3 IP packet showing headers

## Slide 12: Internet Layer Protocols
Concerned with addressing
  Example IP address: 192.168.1.115
Internet Protocol version four (IPv4)
  Older type of addresses
IPv6 is a longer type of address
  Example: 2001:0:4137:9376:43e:2599:3f57:fe9a

## Slide 13: Other Internet Layer Protocols (1 of 2)
Internet Control Message Protocol (ICMP)
  Features called automatically by applications
  Example: ping used to query whether a host is reachable
Notes: Note (p. 133): The TCP/IP model’s Internet layer corresponds roughly to the OSI model’s Network layer.

## Slide 14: Other Internet Layer Protocols (2 of 2)
Figure 6.4 Simplified IP header

## Slide 15: Fields in a Full IP Packet Header
Version
Header length
Differentiated services code point (DSCP)
Time to live (TTL)
Protocol

## Slide 16: Transport Layer Protocols
Determines if the data is:
  Connection-oriented ► Transmission Control Protocol (TCP) or
  Connectionless ► User Datagram Protocol (UDP)
Application-layer protocols determine which protocol is used - TCP or UDP

## Slide 17: TCP (1 of 2)
Used by most TCP/IP applications
Communication rules require sending and receiving machines to acknowledge the other’s presence and readiness
Chops up data into segments
  Each segment has a sequence number
Each application is assigned a specific port number on which to listen/send

## Slide 18: TCP (2 of 2)
Figure 6.5 TCP three-way handshake in action

## Slide 19: Fields in the TCP Header (1 of 2)
Source port and destination port
Sequence and ACK numbers
Flags
Checksum

## Slide 20: Fields in the TCP Header (2 of 2)
Figure 6.6 TCP header

## Slide 21: UDP (1 of 2)
“Fire-and-forget” protocol
Used when data must simply be sent without worrying about a few dropped pieces here and there
Very fast protocol
  Examples: VoIP, DHCP, and DNS
Used by Domain Name System (DNS) and Dynamic Host Configuration Protocol (DHCP)

## Slide 22: UDP (2 of 2)
Figure 6.7 UDP header
Notes: Note (p. 135): You saw this back in Chapter 1, but I’ll mention it again here. Data gets chopped up into chunks at the Transport layer when using TCP. The chunks are called segments with TCP. UDP datagrams don’t get chopped up at the Transport layer; they just get a header.

## Slide 23: Application Layer Protocols (1 of 2)
TCP/IP protocols used to move data back and forth
  Application headers differ between applications
Sample header from HTTP shown in Figure 6.8
Notes: Note (p. 135): I’m simplifying the call and response interaction between a Web server and a Web client. The explanation here is only the first part of the process in accessing a Web page.

## Slide 24: Application Layer Protocols (2 of 2)
Figure 6.8 HTTP header

## Slide 25: IP and Ethernet

## Slide 26: TCP: LANs and WANs
TCP/IP suite supports simple and complex networks
  Small LAN
  Multiple LANs connected to form a WAN

## Slide 27: TCP/IP on LAN over Ethernet (1 of 6)
On small network, sending computer broadcasts using MAC address FF-FF-FF-FF-FF-FF to obtain recipient’s MAC address
Broadcasting is disastrous to a large network

## Slide 28: TCP/IP on LAN over Ethernet (2 of 6)
Figure 6.9 Two addresses

## Slide 29: TCP/IP on LAN over Ethernet (3 of 6)
Figure 6.10 Encapsulation

## Slide 30: TCP/IP on LAN over Ethernet (4 of 6)
Figure 6.11 What is this MAC address?

## Slide 31: TCP/IP on LAN over Ethernet (5 of 6)
Figure 6.12 Sending an ARP request

## Slide 32: TCP/IP on LAN over Ethernet (6 of 6)
Figure 6.13 Computer B responds
Notes: Try This! (p. 137): ARP in Windows
To show Windows’ current ARP cache, open a command line and type
arp –a
You should see results like this:
Interface: 192.168.4.71 --- 0x4
Internet Address Physical Address Type
192.168.4.76 00-1d-e0-78-9c-d5 dynamic
192.168.4.81 00-1b-77-3f-85-b4 dynamic
Now delete one of the entries in the ARP table with this command:
arp –d [ip address from the previous results]
Run the arp –a command again. The line for the address you specified should be gone. Now ping the address you deleted and check the ARP table again. Did the deleted address return?

## Slide 33: IP Addressing
Overcomes limitations of Ethernet networks
Unique IP address per host
Unique address per logical network
Communicate between LANs without constant broadcasts
Notes: Cross Check (P. 138): The OSI Seven-Layer Model
This chapter uses the TCP/IP model to describe the interactions among the various components and protocols involved in a TCP/IP network. But the OSI model is exceptionally important in modern networking, and you should recognize how parts fit into it as well. You learned about this in Chapter 1, so refer back and cross check your knowledge. What layer (number and name) handles the interaction with Ethernet hardware? What about MAC addressing versus IP addressing? Which layers deal with naming?

## Slide 34: IP Addresses (IPv4)
32-bit value
Example: 11000000101010000000010000000010
Broken into four groups of eight 11000000.10101000.00000100.00000010
Each 8-bit value is converted into a decimal number between 0 and 255
Notes: This entire chapter focuses on IPv4

## Slide 35: Binary to Decimal Conversion
Binary | Decimal
00000000 | 0
00000001 | 1
00000010 | 2
00000011 | 3
00000100 | 4
00000101 | 5
00000110 | 6
00000111 | 7
00001000 | 8
(skip a bunch) | (skip a bunch)
Binary | Decimal
11111000 | 248
11111001 | 249
11111010 | 250
11111011 | 251
11111100 | 252
11111101 | 253
11111110 | 254
11111111 | 255

## Slide 36: Binary, Decimal, and Octal Numbering (1 of 2)
Converted address in dotted decimal notation
  11000000101010000000010000000010 is displayed as 192.168.4.2
Know how to convert dotted decimal to binary and back
  Every OS has a calculator
Notes: Check out the two excellent Chapter 6 “Binary Calculator” sims over at http://totalsem.com/007. View the Show!, then practice on the Click!

## Slide 37: Binary, Decimal, and Octal Numbering (2 of 2)
Figure 6.14 Windows (left) and macOS (right) Calculators in Programmer mode
Notes: Note (p. 139): Using a calculator utility to convert to and from binary/ decimal is a critical skill for a network tech. Later on you’ll do this again, but by hand!

## Slide 38: Using a Calculator for Conversions (1 of 2)
Decimal to binary conversion
  Enter a value in decimal view
  Switch to binary view to convert the value
  Leading zeroes do not display in the calculator
  Leading zeroes are important when working with IP addresses

## Slide 39: Using a Calculator for Conversions (2 of 2)
Figure 6.15 Converting decimal to binary with Windows 10 Calculator

## Slide 40: MAC and IP Addressing (1 of 5)
Every MAC address must be unique on a network
Every IP address must be unique
Every computer on a small TCP/IP network has both an IP address and a MAC address
An operating system utility displays addresses
  A command-line utility is also available

## Slide 41: MAC and IP Addressing (2 of 5)
Figure 6.16 A small network with both IP and MAC addresses

## Slide 42: MAC and IP Addressing (3 of 5)
Figure 6.17 macOS Network utility

## Slide 43: MAC and IP Addressing (4 of 5)
Figure 6.19 ipconfig /all results

## Slide 44: MAC and IP Addressing (5 of 5)
Figure 6.20 Results from running ifconfig in macOS
Notes: Exam Tip (p. 143): Make sure you know that ipconfig and ifconfig provide a tremendous amount of information regarding a system’s TCP/IP settings.

## Slide 45: IP Addresses in Action
IP addresses support LANs and WANs
Functions of IP
  Creates a way to use IP addresses so each LAN has its own identification
  Interconnects all LANs using routers
  Gives each computer a way to recognize whether a packet is for the LAN or the WAN

## Slide 46: Network IDs (1 of 2)
All computers on same LAN must share a similar IP address
First group of numbers will be the same
Last group of numbers will be unique

## Slide 47: Network IDs (2 of 2)
Figure 6.22 IP addresses for a LAN
Notes: Note (p. 144): Two things to note here. First, the network ID and the host ID are combined to make a system’s IP address. Second, a host ID can end in 0—although this is uncommon—but we have to discuss subnetting before any of this will make sense. Read on!

## Slide 48: Interconnecting LANs (1 of 5)
Requires a router connection
Router requires an IP address on each LAN
Default gateway
  Router interface
Network administrators often give lowest host address in the network to the router

## Slide 49: Interconnecting (2 of 5)
Figure 6.23 LAN with router

## Slide 50: Interconnecting (3 of 5)
Routers use network IDs to determine network traffic
Routing table
  Instructions that tell the router what to do with incoming packets and where to send them

## Slide 51: Interconnecting (4 of 5)
Figure 6.24 Router diagram
Notes: Note (p. 145): Routing tables are covered in more detail in Chapter 7.

## Slide 52: Interconnecting (5 of 5)
Figure 6.25 LAN, router, and the Internet

## Slide 53: Limitations of Network ID Formats
Number of zero values at the end determines maximum number of hosts
Examples:
  202.120.10.0 limited to 254 addresses
  170.45.0.0 has a total of 65,534 hosts
  12.0.0.0 has a total of 16.7 million hosts
Network IDs allow make it possible to connect multiple LANs into a WAN

## Slide 54: Subnet Mask (1 of 3)
Different processes used to send a packet to local and remote computers
  Local computer: send a broadcast
  Remote computer: send packet to the default gateway
  Processes are illustrated in Figures 6.26 and 6.27
Subnet mask
  String of ones followed by some number of zeros
Notes: Exam Tip (P. 146):
At this point, you should memorize that 0 = 00000000 and 255 = 11111111. You’ll find knowing this very helpful throughout the rest of the book.

## Slide 55: Subnet Mask (2 of 3)
Figure 6.26 The three amigos, separated by walls or miles

## Slide 56: Subnet Mask (3 of 3)
Figure 6.27 Sending a packet remotely

## Slide 57: Using the Subnet Mask (1 of 2)
Line up an IP address with a corresponding subnet mask in binary
  The portion of the IP address that aligns with the ones of the subnet mask is the network ID of the IP address
  The portion of the IP address that aligns with the zeroes is the host ID

## Slide 58: Using the Subnet Mask (2 of 2)
 | Dotted Decimal | Binary
IP address | 192.168.5.23 | 11000000.10101000.00000101.00010111
Subnet mask | 255.255.255.0 | 11111111.11111111.11111111.00000000
Network ID | 192.168.5.0 | 11000000.10101000.00000101.x
Host ID | x.x.x.23 | x.x.x.00010111

## Slide 59: Comparing Addresses (1 of 2)
Steps
  The sending computer compares the destination IP address to its own IP address using the subnet mask
  If the destination IP address matches the computer IP wherever there’s a 1 in the subnet mask, the destination is local
    If not, the address is remote
Notes: Note (p. 147): The explanation about comparing an IP address to a subnet mask simplifies the process, leaving out how the computer uses its routing table to accomplish the goal. We’ll get to routing and routing tables in Chapter 7. For now, stick with the concept of the node using the subnet mask to determine the network ID.

## Slide 60: Comparing Addresses (2 of 2)
Figure 6.28 Comparing addresses

## Slide 61: ARP and the OSI Model (1 of 6)
For a local destination address, sending computer sends out an Address Resolution Protocol (ARP) broadcast to determine the destination computer’s MAC address
  An ARP packet contains the sending computer’s IP address and the destination address

## Slide 62: ARP and the OSI Model (2 of 6)
The destination computer responds by sending an ARP response containing its MAC address
The sending computer can now send data packets to the destination

## Slide 63: ARP and the OSI Model (3 of 6)
Figure 6.29 Comparing addresses again

## Slide 64: ARP and the OSI Model (4 of 6)
Figure 6.30 Sending an ARP request to the gateway

## Slide 65: An Example of a Valid Subnet Mask
11111111111111111111111100000000 = 255.255.255.0
11111111111111110000000000000000 = 255.255.0.0
11111111000000000000000000000000 = 255.0.0.0
11111111111111111111111100000000 = /24 (24 ones)
11111111111111110000000000000000 = /16 (16 ones)
11111111000000000000000000000000 = /8 (8 ones)
Notes: Note (p. 149): By definition, all computers on the same network have the same subnet mask and network ID.

## Slide 66: Tips for Setting Up Subnet Masks
Network administrators must enter the correct IP address and subnet mask when setting up a system
  The networking software does the rest
If you want a computer to work in a routed network, you must configure the computer correctly with an IP address, a subnet mask, and a default gateway

## Slide 67: Class IDs (1 of 2)
No two devices on the Internet can share the same IP address
  Internet Assigned Number Authority (IANA) tracks/disperses IP addresses in network blocks
  IANA oversees several Regional Internet Registries (RIRs)
  RIRs in turn pass out IP addresses to large ISPs
  ISPs pass out IP addresses to most end users
Notes: Note (p. 149): The Internet Corporation for Assigned Names and Numbers (ICANN) manages IANA.

## Slide 68: Class IDs (2 of 2)
 | First Decimal Value | Addresses | Hosts per Network ID
Class A | 1–126 | 1.0.0.0–126.255.255.255 | 16,277,214
Class B | 128–191 | 128.0.0.0–191.255.255.255 | 65,534
Class C | 192–223 | 192.0.0.0–223.255.255.255 | 254
Class D | 224–239 | 224.0.0.0–239.255.255.255 | Multicast
Class E | 240–254 | 240.0.0.0–254.255.255.255 | Experimental
Notes: Exam Tip (p. 149): CompTIA and many techs use the term classful to describe the traditional class blocks. Thus you’ll see classful A, B, C, and D addressing on the exam. Keep reading and this will make sense.

## Slide 69: Ways to Send a Packet
Three ways
  Broadcast to every computer on the LAN
  Unicast from one computer to another computer
  Multicast from one computer to a group
    Often used by routers
Multicast class blocks are often used for one-to-many communication
  Example: streaming video conferencing
Notes: Exam Tip (p. 150): Make sure you memorize the IP class blocks! You should be able to look at any IP address and know its class block. Here’s a trick to help: The first binary octet of a Class A address always begins with a 0 (0xxxxxxx); for Class B, it begins with a 10 (10xxxxxx); for Class C, with 110 (110xxxxx); for Class D, with 1110 (1110xxxx); and for Class E, it begins with 1111 (1111xxxx).

## Slide 70: Class Blocks
IP class blocks were allocated generously at first
  Unallocated IP addresses became scarce
IP class blocks concept did not scale well
  If you needed 2000 IP addresses, you had to take a single Class B or eight Class C blocks
Solution
  Classless Inter-Domain Routing (CIDR)

## Slide 71: CIDR and Subnetting

## Slide 72: CIDR and Subnetting
Subnetting chops up a single class of IP addresses into multiple smaller groups
CIDR and subnetting are virtually the same thing
  Subnetting is done by an organization on a block of addresses to create multiple subnetworks
  CIDR is done by an ISP on a block of addresses to create multiple subnets to pass out to customers
Notes: Exam Tip (p. 150): Expect a question on the exam that compares the loopback and reserved addresses. Loopback are the 129.x.x.x addresses; Reserved are the Experimental addresses.

## Slide 73: Subnetting
Advantages of subnetting
  Allows more efficient use of IP addresses than class blocks
  Enables separation of networks for security
  Ensures bandwidth control
Subnet mask is cornerstone of subnetting
  Extend subnet masks of /8, /16, or /24 subnet by adding more ones (removing equal number of zeroes)
Notes: Exam Tip (p. 150): You need to know how to subnet to pass the CompTIA Network+ exam.

## Slide 74: An Example of Subnetting (1 of 4)
Subnetting an Internet café
  50 computers
    40 public computers
    10 back office computers
    10 wireless clients (maximum)
  Network ID 192.168.4/24
  Must prevent people using the public system from accessing the private machines

## Slide 75: An Example of Subnetting (2 of 4)
Figure 6.31 Layout of the network

## Slide 76: An Example of Subnetting (3 of 4)
Begin with the given subnet mask and move it to the right until you have the number of subnets you need
Forget the dots
  Don’t be limited to /8, /16, /24 networks
  Network IDs do not need to end on the dots
  Create subnets of /26, /27, /22, and so on

## Slide 77: An Example of Subnetting (4 of 4)
192.168.4.0/24
Change a zero to a one in the subnet mask
/24 becomes a /25 subnet
  11111111111111111111111110000000

## Slide 78: Calculating the Maximum Number of Hosts (1 of 2)
Example: hosts on a /24 network
  192.168.4.1 to 192.168.4.254 = 254 hosts
  Calculate in binary
    In a /24 network, eight binary digits are used for the host ID
    00000001 to 11111110 = 254 hosts
    28 – 2 = 254 total hosts
  Memorize the formula for the number of hosts
    2x – 2 (x = the number of zeroes in the subnet mask)
Notes: Note (p. 151): Classful subnets are always /8, /16, or /24. When we stop using that convention and start using classless subnet masks, we are using a custom subnet mask.

## Slide 79: Calculating the Maximum Number of Hosts (2 of 2)
Maximum number of hosts on a /16 network
  In a /16 network, 16 zeroes are part of the host ID
  216 – 2 = 65,534 total hosts
Maximum number of hosts on a /26 network
  In a /26 network, 6 zeroes are part of the host ID
  26 – 2 = 62 total hosts

## Slide 80: Your First Subnet (1 of 3)
Convert the 192.168.4.0/24 network ID into three network IDs
Write out the subnet mask in binary
Place a line at the end of the ones
  See Figure 6.32
Draw a second line one digit to the right
  See Figure 6.33
Notes: Note (p. 152): You cannot subnet without using binary!

## Slide 81: Your First Subnet (2 of 3)
Figure 6.32 Step 1 in subnetting

## Slide 82: Your First Subnet (3 of 3)
Figure 6.33 Organizing the subnet mask

## Slide 83: The Format of a Subnet Mask (1 of 2)
The subnet mask is now separated into three areas (these are not in official terms)
  Default Subnet mask (DSM)
  Network ID extension (NE)
  Hosts (H)
This is now a /25 subnet mask

## Slide 84: The Format of a Subnet Mask (2 of 2)
A subnet mask is always 32 binary digits long
A string of ones followed by a string of zeroes
11111111111111111111111110000000
Put periods between every eight digits
11111111.11111111.11111111.10000000
Then convert to dotted decimal
The resulting subnet mask: 255.255.255.128

## Slide 85: Other Types of Subnet Masks
Subnet masks can and do use more than 255s and 0s (in dotted decimal form)
Examples of legitimate subnet masks
  255.255.255.224
  255.255.128.0
  255.248.0.0

## Slide 86: Calculating Subnets (1 of 2)
Start with a beginning subnet mask
Extend the subnet extension until you have the number of subnets you need
Formula is 2y, where y is number of bits added to the subnet mask

## Slide 87: Calculating Subnets (2 of 2)
Figure 6.34 Initial subnetting

## Slide 88: Subnet /24 to /26 (1 of 3)
Adds two digits, creating four new network IDs
Convert the original network ID to binary and add the four different network ID extensions to the end

## Slide 89: Subnet /24 to /26 (2 of 3)
Figure 6.35 Creating the new network IDs

## Slide 90: Subnet /24 to /26 (3 of 3)
Figure 6.36 New network ID address ranges

## Slide 91: The New Network IDs in Decimal (1 of 2)
Network ID | Host Range | Broadcast Address
192.168.4.0/26 | (192.168.4.1–192.168.4.62) | 192.168.4.63
192.168.4.64/26 | (192.168.4.65–192.168.4.126) | 192.168.4.127
192.168.4.128/26 | (192.168.4.129–192.168.4.190) | 192.168.4.191
192.168.4.192/26 | (192.168.4.193–192.168.4.254) | 192.168.4.255
Notes: Note (p. 154): If wasting subnets seems contrary to the goal of efficient use, keep in mind that subnetting has two goals: efficiency and making multiple network IDs from a single network ID. This example is geared more toward the latter goal.

## Slide 92: The New Network IDs in Decimal (2 of 2)
Figure 6.37 Three networks using the new network IDs

## Slide 93: Creating a /27 subnet (1 of 4)
Move the NE over three digits
Calculate the host address ranges for each usable new subnet

## Slide 94: Creating a /27 subnet (2 of 4)
Figure 6.38 Moving the network ID extension three digits

## Slide 95: Creating a /27 subnet (3 of 4)
Figure 6.39 Two of the eight network ID address ranges
Notes: Exam Tip (p.155): CompTIA and many techs refer to a CIDR address as a classless address, meaning the subnet used doesn’t not conform to the big four on the classful side: A, B, C, or D. When you see that term on the exam, you’ll know you should look for subnetting.

## Slide 96: Creating a /27 subnet (4 of 4)
192.168.4.0/27 (192.168.4.1 – 192.168.4.30)
192.168.4.32/27 (192.168.4.33 – 192.168.4.62)
192.168.4.64/27 (192.168.4.65 – 192.168.4.94)
192.168.4.96/27 (192.168.4.97 – 192.168.4.126)
192.168.4.128/27 (192.168.4.129 – 192.168.4.158)
192.168.4.160/27 (192.168.4.161 – 192.168.4.190)
192.168.4.192/27 (192.168.4.193 – 192.168.4.222)
192.168.4.224/27 (192.168.4.225 – 192.168.4.254)
Notes: Tech Tip: ISPs and Classless Addresses (p. 155)
If you order real, unique, ready-for-the-Internet IP addresses from your local ISP, you’ll invariably get a classless set of IP addresses. More importantly, when you order them for clients, you need to be able to explain why their subnet mask is 255.255.255.192, when all the books they read tell them it should be 255.255.255.0!
All this assumes you can get an IPv4 address by the time you’re reading this book. See Chapter 12 for the scoop on IPv6, the addressing scheme of the future.

## Slide 97: Manual Dotted Decimal to Binary Conversion
Write bit values in decimal from left to right
Take binary value and place ones and zeroes under appropriate positions
    128 64 32 16 8 4 2 1
    1 0 0 1 0 1 1 0
Add the decimal values that have a 1 underneath
    128 + 16 + 4 + 2 = 150

## Slide 98: Manual Decimal to Binary Conversion (1 of 2)
Manually converting 221 decimal to binary
  Start with bit values beginning with 128
  Place decimal value above the first value on the left which it exceeds and subtract and place a one to represent this binary value
    221
    128 64 32 16 8 4 2 1
    93
  1

## Slide 99: Manual Decimal to Binary Conversion (2 of 2)
Place the remainder above the next bit value that it exceeds (place a zero in positions that are skipped)
    93 29 29 13 5 1
    128 64 32 16 8 4 2 1
    29 13 5 1
  1 1 0 1 1 1 0 1
  Decimal 221 = binary 11011101
Notes: Exam Tip (p. 157): Make sure you can manually convert decimal to binary and binary to decimal.

## Slide 100: CIDR: Subnetting in the Real World
Two situations in which subnetting takes place
  ISPs receive network blocks from IANA and subnet for customers
  Very large customers take subnets from ISPs and make their own subnets
Notes: Exam Tip (p. 157): Expect to see a question or two on the CompTIA Network+ exam that asks you to compare CIDR notation (IPv4 vs. IPv6). The former should be familiar, with four octets and a /# for the subnet mask. See Chapter 12 for IPv6.

## Slide 101: Why Learn Subnetting?
The CompTIA Network+ exam requires it
There is a good chance you will contact an ISP and get CIDR addresses
  Think of subnets in terms of CIDR values like /10, /22, /26, and so on
More advanced IT certifications (Cisco, Microsoft, and so on) require this knowledge

## Slide 102: IP Address Assignment

## Slide 103: Giving a Computer an IP Address
Static addressing
  Type in all the information
Dynamic addressing
  Server automatically passes out IP information to systems as they connect to the network
Notes: Exam Tip (p. 158): The CompTIA Network+ exam objectives call the methods for setting up devices for IP addresses IP address assignment. Note that that term applies to both static and dynamic methods (discussed here).

## Slide 104: Static IP Addressing (1 of 2)
Class C network block for 197.156.4.0/24
  You can do whatever you want with your own network ID
  Use a legitimate IP address and subnet mask for the network ID
  Every IP address must be unique
  You do not have to use the numbers in order
  You do not have to use 197.156.4.1 as the default gateway

## Slide 105: Static IP Addressing (2 of 2)
Figure 6.40 A small network

## Slide 106: Static IP Addressing: Common Principles (1 of 5)
Give the default gateway the first host IP address in the network ID
  Try to use the IP addresses in some kind of sequential order
  Try to separate servers from clients
    Servers host addresses: 197.156.4.10 to 197.156.4.19
    Client host addresses: 197.156.4.200 to 197.156.4.254
Write down whatever you do so the person who comes after you understands

## Slide 107: Static IP Addressing: Common Principles (2 of 5)
Give each computer an IP address, subnet mask, and default gateway
  Windows: Internet Protocol Version 4 (TCP/IPv4) Properties dialog box
  macOS: Network utility in System Preferences
  UNIX/Linux: ifconfig command from the command line: address will be lost upon reboot
  Network Configuration program in Ubuntu Linux distro

## Slide 108: Static IP Addressing: Common Principles (3 of 5)
Figure 6.41 Entering static IP information in Windows Internet Protocol Version 4 (TCP/IPv4) Properties
Notes: Exam Tip (p. 159): You might get a question about setting a static IP address in Linux where ip isn’t one of the choices. Go with the deprecated ifconfig command in that case.
Check out the excellent “Static IP in Linux” Show! over at http://totalsem.com/007. It’ll take you through the process of setting up a static IP in a typical Linux distro.

## Slide 109: Static IP Addressing: Common Principles (4 of 5)
Figure 6.42 Entering static IP information
in the macOS Network utility

## Slide 110: Static IP Addressing: Common Principles (5 of 5)
Figure 6.43 Ubuntu’s Network Configuration utility

## Slide 111: Verifying with ping (1 of 2)
Always verify with the ping command
If the ping is not successful
  Check your IP settings
  Check connections, driver, and so on
Static addressing is still used for most critical systems
Most systems today use dynamic IP addressing
Notes: Caution (p. 160): Always verify with ping—it’s too easy to make a typo when you entering static IP addresses.
Exam Tip (p. 160):
A very early protocol called Bootstrap Protocol (BOOTP) preceded DHCP in providing dynamic IP addressing. It’s been dead for many decades, but has been known to appear, zombie-like, on CompTIA exams. If you see BOOTP or BootP, substitute DHCP and you’ll see the right answer.

## Slide 112: Verifying with ping (2 of 2)
Figure 6.44 Two pings (successful ping on top, unsuccessful ping on bottom)

## Slide 113: Dynamic IP Addressing (1 of 2)
Dynamic Host Configuration Protocol (DHCP) automatically assigns an IP address when a computer connects to the network
DHCP process
  A computer is configured to use DHCP
  Every OS has a method to tell a computer to use DHCP
Notes: Note (p. 161): Using the acronym DORA— for Discover, Offer, Request, and Acknowledgement—will help you remember the DHCP four-way handshake.
Exam Tip (p. 161): DHCP uses UDP ports 67 and 68. And yes, memorize the numbers.
Check out the excellent Chapter 6 “DHCP Client Setup” Click! over at http://totalsem .com/007. It walks you through the process of setting up DHCP in Windows.

## Slide 114: Dynamic IP Addressing (2 of 2)
Figure 6.49 Setting up for DHCP

## Slide 115: How DHCP Works (1 of 5)
The DHCP server is configured to pass out IP addresses to DHCP clients
  Scope = range of IP addresses
  Subnet mask for scope
  Default gateway for scope
  Other options (default gateway, DNS server, network time server, and more)

## Slide 116: How DHCP Works (2 of 5)
Figure 6.50 DHCP server main screen

## Slide 117: How DHCP Works (3 of 5)
Figure 6.52 DHCP relays enable DHCP traffic to cross routers
Notes: Note (p. 163): The CompTIA objectives list DHCP TTL (Time to Live?) as something of interest. As a 25-year user of DHCP, I’ve never had this issue. After much research, there are some DHCP clients that need a TTL setting to determine how many routers (hops) a DHCP relay can be from the IP helper. I say “Nuts” to CompTIA.

## Slide 118: How DHCP Works (4 of 5)
Figure 6.56 DHCP Server configuration screen

## Slide 119: How DHCP Works (5 of 5)
Figure 6.57 DHCP Server Options screen

## Slide 120: Living with DHCP (1 of 2)
Very popular
Possible problems
  DHCP client tries to get a DHCP address and fails
    OS will post an error
    The DHCP client will have an address in the 169.254.0.0/16 network ID
    This special address is generated by a version of zero-configuration networking (zeroconf ); example – Microsoft’s Automatic Private IP Addressing (APIPA)

## Slide 121: Living with DHCP (2 of 2)
Figure 6.58 DHCP error in Windows 7

## Slide 122: APIPA (1 of 2)
APIPA allows computers on a single network to communicate
  No default gateway
  Clients using APIPA cannot access the Internet
  Use an available tool to check IP address
  If you see an APIPA address, you know you have a DHCP problem
Notes: Exam Tip (p. 166): Systems that use static IP addressing can never have DHCP problems.

## Slide 123: APIPA (2 of 2)
Figure 6.59 Network utility in System Preferences

## Slide 124: Reestablish the Lease Manually
Windows: ipconfig /renew
Mac: Network utility under System Preferences
May need to force the release
  Windows command line: ipconfig /release; ipconfig /renew
  Linux: sudo ifconfig eth0 down; sudo ifconfig eth0 up
Notes: Exam Tip (p. 166): CompTIA loves TCP and UDP port numbers, so make sure you know that DHCP and BOOTP servers use UDP port 67 and clients use port 68.

## Slide 125: Special IP Addresses (1 of 2)
Loopback address: 127.0.0.1
  Use to send packets from a device to itself
  Use with the ping command
Notes: Exam Tip (p. 167): Make sure you know how to configure your computers to use static IP addressing and know that you use ping to ensure they can communicate. For dynamic IP addressing, make sure you know DHCP. Understand that each client must have some way to “turn on” DHCP. Also understand the concept of a DHCP client and a DHCP server. Be comfortable with APIPA and releasing and renewing a lease on a client.
Note (p. 168): Good network admins always know their network IDs!
Exam Tip (p. 168): Even though, by convention, you use 127.0.0.1 as the loopback address, the entire 127.0.0.0/8 subnet is reserved for loopback addresses! You can use any address in the 127.0.0.0/8 subnet as a loopback address.

## Slide 126: Special IP Addresses (2 of 2)
Private IP addresses
  10.0.0.0 through 10.255.255.255 (1 Class A network block)
  172.16.0.0. through 172.31.255.255 (16 Class B network block)
  192.168.0.0 through 192.168.255.255 (256 Class C network block)
All other IP addresses are public IP addresses
Notes: Exam Tip (p. 168): Make sure you can quickly tell the difference between a private IP address and a public IP address for the CompTIA Network+ exam. The objectives mention the distinction as private vs. public.